M503
; Configuration file for Mini Kossel Release 3 kit from Think3DPrint3D

; Communication and general
M111 S0 ; Debug off
M550 PMiniKossel1 ; Machine name and Netbios name (can be anything you like)
M551 Preprap ; Machine password (used for FTP)
M540 P0xBE:0xEF:0xDE:0xAD:0xFE:0xED ; MAC Address
;*** Adjust the IP address and gateway in the following 2 lines to suit your network
M552 P0.0.0.0 ; Un-comment for DHCP
;M552 P192.168.1.14 ; IP address, comment for DHCP
;M554 P192.168.1.255 ; Gateway, comment for DHCP
;M553 P255.255.255.0 ; Netmask, comment for DHCP
M555 P2 ; Set output to look
like Marlin
;M584 X0 Y1 Z4 E3 ; Move Z motor to driver 4, which is labelled E3 on the board. Original Z driver. Z motors has been moved to the E1 labelled driver position i on the board, since the original position for the Z motor driver 2 has failed.
G21 ; Work in millimetres
G90 ; Send absolute coordinates...
M83 ; ...but relative extruder moves

;Turn off fans: by default PWM fans on Duet V0.8.5 are inverted
M106 I1 ; fans are inverting
M106 S0 ; Turn off Fan 0

; Axis and motor configuration
M569 P0 S1 ; Drive 0 goes forwards
M569 P1 S1 ; Drive 1 goes forwards
M569 P2 S1 ; Drive 2 goes forwards
M569 P3 S1 ; Drive 3 goes forwards
M569 P4 S1 ; Drive 4 goes forwards
M574 X2 Y2 Z2 S1 ; set endstop configuration (all endstops at high end, active high)
;*** The homed height is deliberately set too high in the following - you will adjust it during calibration
M665 R104.05 L215.00 B85 H239.23 ; set delta radius, diagonal rod length, printable radius and homed height
M666 X-0.2 Y-0.05 Z0.25 ; put your endstop adjustments here, or let auto calibration find them
M92 X80 Y80 Z80 ; Set axis steps/mm
M906 X1000 Y1000 Z1000 E1000 ; Set motor currents (mA)
M201 X1000 Y1000 Z1000 E1000 ; Accelerations (mm/s^2)
M203 X20000 Y20000 Z20000 E3600 ; Maximum speeds (mm/min)
M566 X1200 Y1200 Z1200 E1200 ; Maximum instant speed changes mm/minute

; Thermistors
;*** If you have a Duet V0.6 board NOT stickered "4