Modification to Duet3 Expansion1 board v0.9 to correct temperature sensor SPI bus
The modification requires the signals from the 2x5-way header that are originally connected to pins 43, 21 and 23 of the microcontroller to be rerouted to pins 56, 57 and 69 respectively. However, leaving the original pins still connected too is acceptable. So no traces need to be cut.
I have avoided soldering wired directly to MCU pins except in the one case that it is unavoidable, because of the risk of bridging pins.
Procedure:
1. If R76 and R77 have been fitted, remove them.
2. Use a scalpel or similar to remove the solder resist from a portion of the trace connecting pin 23 of the MCU, for example where it passes R78 to the southwest.
3. Use a scalpel or similar to remove the solder resist from the trace connecting pin 43 of the MCU to the nearby via.
4. Apply no-clean flux to the two traces in #2 and #3 and tin them with solder. Also apply flux to pin 57 of the MCU and tin it with solder, taking care not to bridge it to adjacent pins.
5. Connect a wire between pin 57 of the MCU and the end of R78 closest to the MCU. This is the lower green wire in the diagram below
6. Connect a wire between the trace exposed at #3 above and the pad of R77 closest to the MCU. This is the upper green wire in the diagram below.
7. Connect a wire between the trace in #2 above and the pad of R76 closest to the MCU. This is the middle green wire in the diagram below.

See over for diagram and photo.

D Crocker, 2019-07-31

Diagram:

Photo: